ALU:

Function unit. Arithmetic/logic operation.

General registers. 32-bit or 64-bit. AX, BX, …

Status registers. Flags, address of interrupt vector, processor mode (user mode, system mode)

CU: control operations performed in CPU. P. 122. (See slide)

Fetch unit: load the instruction from memory to register and PC (program counter) updates.

Decode unit: determine the type of operation: arithmetic: + - * / , logic: AND OR XOR NOT; fetch operands if needed: load operands form memory to register and ALU

Execution unit: ALU does operation; write register; set flags. Store output if needed: output data to memory.

Memory: store instructions and data. P. 124. (see slide)

Memory address register (MAR): store address of data.

Memory data register (MDR): store the data.

Command register (CMDR): store the command to perform the operation.

Devices:

Storage devices (block-oriented): hard disk, floppy, CD-ROM disc.

Communication (I/O) devices (character-oriented): keyboard, mouse, monitor, and printer.

Device controller connects the device to CPU. Drives.

Device manager (driver) is the software to manage the communication between CPU/memory and devices. Part of OS.

Device-controller-software relationship. P.126 (See slide).

Device controller interface. P.128 (See slide).

Example: Performing a Write (to device1) Operation. P.127

while(device1.busy || device1.done)

<waiting>;

device1.data[0] = <value to write>

device1.command = WRITE;

while(device1.busy)

<waiting>;

device1.done = TRUE;

Devices are much slower than CPU; CPU waits while device operates

CPU may run a different process while I/O is in process

Device driver implements the device management in OS. Device driver and device controller work together to implement CPU-I/O Devices parallelism. Use interrupt.

#### Memory-mapped I/O. P.130

Traditional: separate device address; needs additional I/O instructions.

copy_in R3, 0x012, 4

; copy contents of data register #4 int the controller with device address 0x012

Memory-mapped I/O devices: use extended memory addresses for devices. Reduce  CPU instruction sets.

Mov R3, 0xFFFF0124

See slide.

# Text boxes

MOV   R3,b

MOV   R4,c

ADD   R3,R4

MOV   a, R3

To/from Primary Memory

Result

Right Operand

Left Operand

Functional Unit

Status Registers

. . .

Rn

R2

R1